## Slide 1: Field Cage Simulation Study for Prototype Cherenkov TPC
Michael Phipps, Bob Azmoun, and Craig Woody

## Slide 2: Cherenkov TPC Update
Field cage ordered
Candidate gas studies completed:
  80 Ne/10 CH4/10 CO2
  85 Ne/10 CH4/5 CO2
  85 Ne/5 CH4/10 CO2
TPC chevron readout board analysis … 4 designs w/ 2 mm pitch
  Fine/coarse chevrons
  Fine/coarse floating strip chevrons
Field cage simulation studies … both readout modes:
  TPC
  Combined Cherenkov TPC
Prototype construction begins this fall at BNL

## Slide 3
Field Cage Design
Dimensions: 144.4 x 144.4 x 115.35 mm
Strip insulation: 2 mm thick kapton foil
Strips: Mirrored layers of 26 inner/outer strips on either side of kapton
Strip details: 25 full strips of 3.9 mm length; 1 half strip of 1.9 mm length;
Strip spacing: 0.1 mm strip spacing
Removable fourth wall: to allow for two modes of testing (TPC or Cherenkov TPC)
Top bottom electrodes: Copper top plate; bottom TPC readout: mesh, triple GEM and readout board
Field Cage Simulation Geometry
Simulation software: ANSYS Multiphysics
Dimensions: Same with no mesh or GEM stack or readout components
Strips: Same. 26 mirrored inner/outer strips with kapton insulation
Strip spacing: Approximated to 0.5-1.5 mm to limit problem size
Material attributes: electrodes: ~infinite permittivity; gas: 1.0 permittivity; kapton: 3.5 permittivity
Field Cage Simulation Meshing
Finite element method Ansys simulation
Element shape: 3d tetrahedral
Nodes: 4/element
Meshing size: very fine element sides along electrode strips/spacing where there’s a lot of detail; coarse mesh in large homogenous regions (gas/top and bottom electrodes)

## Slide 4
Preliminary proof-of-concept results
from ANSYS simulations
Note:
2 Scenarios initially tested:
  Parallel Plates (144 mm long) at distance of 110 mm
  4 field cage walls of strips (144 mm) with NO parallel plates

## Slide 5
Parallel Plate Field Map (No Strips)
Distance: ~110 mm; Length: ~144 mm
4 Sides of Strips; No Parallel Plates
EF Sum
ANSYS
Contour Plots of
Absolute Field
EF Sum
ROOT
COLZ Plots of
Percent Discrepancy
Of Field Strength
DIFFERENT SCALES!
Axes Rotated!

## Slide 6
Preliminary results from
ANSYS simulations of TPC field cage
Note:
Cherenkov component not included (All 4 stripped walls symmetric)
Strip spacing approximated due to simulation memory requirements
Scenario: 3 different strip spacing
  0.5 mm spacing
  1.0 mm spacing
  1.5 mm spacing

## Slide 7
0.5 mm Strip Spacing: Scale 1
1.5 mm Strip Spacing: Scale 1
1.0 mm Strip Spacing: Scale 1
0.5 mm Strip Spacing: Scale 2
1.0 mm Strip Spacing: Scale 2
1.5 mm Strip Spacing: Scale 2

## Slide 8
Preliminary results from ANSYS simulations of
Cherenkov TPC field cage
Note:
Geometry: 3 planes of strips w/ 1 wire plane
Wire plane: 52 wires of 0.5 mm diameter (wires in real design ~0.2 mm diameter)
Wire shape: Approximated using block volumes
Strip spacing: Approximated to 1.0 mm
Scenario tested: 4 walls of strips vs. 3 walls of strips + 1 wall of wires

## Slide 9: TPC Cherenkov Geometry

## Slide 10
TPC + Cherenkov: Scale 1 (3 strip planes; 1 wire plane)
TPC + Cherenkov: Scale 2 (3 strip planes; 1 wire plane)
TPC: Scale 1 (4 strip planes)
TPC: Scale 1 (4 strip planes)
Wire Plane